Installation for a Skimmer on an Above-Ground Metal Pool with a Factory Pre-Cut Hole:

- Install vinyl liner in assembled pool.

- Position Double Gasket through square hole in the pool wall. The gasket should surround the edges of the pool wall.

- Position face plate. Weir Door pivot pins should be positioned on the bottom.

- Attach the face plate by lining up through the liner with the gasket and attach to the skimmer body on the outside of the pool.

- Cut out vinyl liner along inside edges of the face plate opening.